## Slide 1: BVMS 13.0 Blueprints
Updated: Jul 2025
BVMS 11.1.1
Blueprints
Notes: Welcome to the BVMS blueprints. This overview explains the deployment scenarios of a typical BVMS or DIVAR IP-based video surveillance system. To design the optimized storage architecture according to the customers requirements, please, use the BVMS Checklist or submit your project to our application designers team.

## Slide 2: Different key components
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
DIVAR IP AIO
VRM
VSG
iSCSI
HW DYNAMIC TRANSCODING
BVMS Server
Licensing
User Authorizations
System logging (SQL)
Alarm management
Configuration management
Operator client
Monitor Wall
DSA E-series
iSCSI only
HIGH DENSITY
1250 MB WRITE/READ
Support VRM based Multipathing for cameras
VRM Server
RECORDING MANAGEMENT
2000 CAMERAS
2 MILLION OF 1Gbit/s BLOCKS
STORAGE VIRTUALIZATION
Video Streaming Gateway
ONVIF CAMERAS
H264 via RTSP
JPEG via HTTP
32 CHANNELS / VSG
BVMS Blueprints
Notes: Let’s start with an overview of the components. The BVMS management server is responsible for licensing, user authorization, logs, configuration management, and alarm management. The video surveillance operator uses the operator client to look at live and recorded video, processes alarms, and monitors the security situation of an environment. The decoders, driving a monitor wall, assist a team of operators to collaboratively solve security incidents. The VRM server is responsible for the recording management of up to 2000 cameras. The DIVAR IP (All-in-one) serves as an all-in-one BVMS system or a video surveillance storage device. The DSA E-series are a high performance video surveillance iSCSI storage system. Last, the video streaming gateway acts as a bridge between the Bosch video surveillance components and ONVIF cameras.

## Slide 3
BVMS PROFESSIONAL
Plus
LITE
BVMS
Lite, Plus, Professional
Notes: BVMS comes in three editions: Professional, Plus, and Lite. The deployment scenarios presented in this section are valid for all editions, considering their limitations. For example, BVMS Lite can manage up to 42 cameras, BVMS Plus can manage up to 256 cameras, and BVMS Professional can manage up to 2000 cameras.

## Slide 4: BVMS all in one
Operator client
BVMS Server
VRM Server
DIVAR IP AIO iSCSI only
Cameras
500*
max
CLIENTS
10
max
DIVAR IP AIO
iSCSI only
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
* Max 500 devices (cameras, replays, inputs, etc.) in logical tree if BVMS MS and VRM server on the same hardware
VSG
iSCSI
HW DYNAMIC TRANSCODING
BVMS Blueprints
Notes: The BVMS management server and VRM can run on one physical server when the video surveillance system does not have over 500 cameras. In this case, the DIVAR IP All-in-one devices or a DSA E-series can act as storage devices. The DIVAR IP All-in-one can also act as a VSG or transcoding resource.

## Slide 5: Embedded VRM’s
Operator client
BVMS Server +
VRM
CAMERAS
500
max
CLIENTS
100
max
DIVAR IP AIO 7000
VRM
125
max
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
VRM
VSG
iSCSI
HW DYNAMIC TRANSCODING
iSCSI array NETAPP
BVMS Blueprints
Notes: The VRM can also be distributed on the DIVAR IP all-in-ones that act as video surveillance storage. Each VRM, running on a DIVAR IP all-in-one 7000 can manage up to 256 cameras. A VRM running on a DIVAR IP all-in-one 5000 can manage up to 42 cameras.

## Slide 6: Dedicated VRM
Operator client
BVMS Server
CAMERAS
2000
max
CLIENTS
100
max
NOIR = 100Mbit/sits
BLEU = 1Gbit/sits
VERT = 1Gbit/sits - 10Gbit/sits
VRM
125
max
VRM Server
iSCSI array NETAPP
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
DIVAR IP AIO
iSCSI only
BVMS Blueprints
Notes: We recommend to install a separate VRM server for larger video surveillance installations.

## Slide 7: Dedicated VRM & Failover
Operator client
BVMS Server
CAMERAS
2000
max
CLIENTS
100
max
VRM
125
max
VRM Server
iSCSI array NETAPP
VRM Server
“Failover”
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
DIVAR IP AIO
iSCSI only
BVMS Blueprints
Notes: Projects that require redundant replay capabilities need an additional fail-over VRM server. The fail-over servers takes over the replay and block distribution functionality of the primary VRM if it fails.

## Slide 8: Distributed storage
Operator client
BVMS Server
CAMERAS
2000
max
CLIENTS
100
max
VRM
125
max
VRM Server
iSCSI array NETAPP
Building A “Pool X”
Building B “Pool Z”
DIVAR IP AIO
iSCSI only
DIVAR IP AIO
iSCSI only
iSCSI array NETAPP
POOL
120/VRM
max
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
BVMS Blueprints
Notes: There are two options when storage devices are located in multiple buildings on a campus. You can distribute the storage and centralize the VRM. This reduces the (maintenance) cost of the system, but also reduces the resilience and performance.

## Slide 9: Distributed VRM’s
Operator client
BVMS Server
CAMERAS
2000
max
CLIENTS
100
max
VRM
125
max
VRM Server
iSCSI array NETAPP
Building A “VRM A”
Building B “VRM B”
DIVAR IP AIO iSCSI only
DIVAR IP AIO
iSCSI only
iSCSI array NETAPP
VRM Server
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
BVMS Blueprints
Notes: When you distribute VRMs you increase the replay performance of the system and you create virtual problem domains. This makes it easier to troubleshoot recording and replay issues. Additionally, if one VRM fails, the failure is limited to a specific part of the system.

## Slide 10: Mirrored recording
BVMS Server
CAMERAS
2000
max
CLIENTS
100
max
Primary VRM Server
iSCSI array NETAPP
Primary storage
DIVAR IP AIO iSCSI only
DIVAR IP AIO
iSCSI only
iSCSI array NETAPP
Secondary VRM Server
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
Mirrored storage
Same stream on both storage
Same stream on both storage
Same stream on both storage
BVMS Blueprints
Notes: Mirrored recording duplicates the video on two identical storage devices. If one storage devices fails, the operator can continue to replay video footage from the second storage device.

## Slide 11: Dual recording
BVMS Server
CAMERAS
2000
max
CLIENTS
100
max
Primary VRM Server
iSCSI array NETAPP
Primary storage
DIVAR IP AIO iSCSI only
DIVAR IP AIO
iSCSI only
iSCSI array NETAPP
Secondary VRM Server
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
Dual storage
Quality 1
Quality 2
Frame Rate 1
Frame Rate 2
One storage only
BVMS Blueprints
Notes: Dual recording is similar to mirrored recording, but allows you to change the quality of the video that is stored on the second storage device. This allows operators to replay video from the second video storage device when the primary device has failed, while keeping the costs under control.

## Slide 12
SCALABILITY
BVMS ENTERPRISE
Notes: BVMS Enterprise allows you to connect multiple BVMS systems, including DIVAR IP all-in-one. The video surveillance operator can access all systems from a single client application and has full control over these systems.

## Slide 13: Enterprise environment – Multi-servers
BVMS Professional
Operator client
BVMS Professional Server
VRM Server
iSCSI array NETAPP
Sub-system A
Sub-system B
DIVAR IP AIO
BVMS Server
DIVAR IP AIO 7000
Operator client
Operator client
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
Up to 100 subsystems connected to EMS
Up to 2.000 cameras per subsystem.
Up to 100 Enterprise user-groups.
Up to 14.000 cameras per user-group (Note: Performance workstation required, min.16GB RAM for the Enterprise Operator Client
Subsystems: BVMS (Lite, Plus, Professional), DIVAR IP AIO 4000/6000/7000
Minimum speed: 10Mbit/s.
Recommended speed: 100Mbit/s
(network speed has an impact on the start-up time of the enterprise operator client and the number of video streams that can be displayed).
CAMERAS
14.000
max
CLIENTS
100
max
SUBSYSTEMS
100
max
BVMS Blueprints
We recommend to use a secure connection, for example, SSH or VPN, to allow multiple locations to communicate.
Notes: BVMS Enterprise can handle up to 100 subsystems. One video surveillance operator can access up to 14.000 cameras at the same time. In this case we assume that the entire system is connected to a private (or transparent) network. The Enterprise Operator Client communicates directly to the subsystem and the devices located in the context of the subsystem.

## Slide 14: Enterprise – BVMS Plus
BVMS Plus
Operator client
BVMS Plus Server (or DIVAR IP AiO 7000)
VRM Server
iSCSI array NETAPP
Sub-system A
Sub-system B
DIVAR IP AIO
BVMS Server
DIVAR IP AIO 7000
Operator client
Operator client
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
Minimum speed: 10Mbit/s.
Recommended speed: 100Mbit/s
(network speed has an impact on the start-up time of the enterprise operator client and the number of video streams that can be displayed).
CAMERAS
14.000
max
CLIENTS
100
max
SUBSYSTEMS
20
max
We recommend to use a secure connection, for example, SSH or VPN, to allow multiple locations to communicate.
BVMS Blueprints
Up to 20 subsystems connected to EMS
Up to 2.000 cameras per subsystem.
Up to 100 Enterprise user-groups.
Up to 14.000 cameras per user-group (Note: Performance workstation required, min.16GB RAM for the Enterprise Operator Client
Subsystems: BVMS (Lite, Plus), DIVAR IP AIO 4000/6000/7000
Notes: BVMS Enterprise bason BVMS Plus can handle up to 20 subsystems. One video surveillance operator can access up to 14.000 cameras at the same time. In this case we assume that the entire system is connected to a private (or transparent) network. The Enterprise Operator Client communicates directly to the subsystem and the devices located in the context of the subsystem.

## Slide 15: Enterprise – Multi-servers (SSH)
BVMS
Operator client (Enterprise)
BVMS Enterprise Server
(Plus or Professional)
VRM Server
iSCSI array NETAPP
Sub-system A
Sub-system B
DIVAR IP AIO
BVMS Server
DIVAR IP AIO
Operator client
Operator client
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
SSH connectivity between Enterprise Operator client and Enterprise subsystem.
BVMS Management Server or DIVAR IP AIO can route at least 50Mbit/s between Enterprise network and video network.
BVMS Server or DIVAR IP AIO acts as bridge between Enterprise and Video network.
Minimum speed: 10Mbit/s.
Recommended speed: 100Mbit/s
(network speed has an impact on the start-up time of the enterprise operator client and the number of video streams that can be displayed).
BVMS Blueprints
We recommend to use a secure connection, for example, SSH or VPN, to allow multiple locations to communicate.
Notes: In this case we assume the system runs on a larger public network. The BVMS management server or DIVAR IP all-in-one is used as a gateway between the local video surveillance network and the corporate network that hosts the Enterprise environment. The Enterprise operator client connects to the management server of the subsystem. The management server routes traffic between the video surveillance network and corporate network.

## Slide 16
LOW BANDWIDTH CONNECTIONS
BVMS
Unmanaged sites
Notes: Unmanaged sites offers, compared to BVMS Enterprise, reduced functionality but increased scalability.

## Slide 17: Unmanaged sites
Operator client
BVMS Server
CLIENTS
100
max
SITES
9999
max
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
RED = >1Mb
Site 1
DVR 400 series
Site 2
DVR 600 series
Site 3
DVR 700 series
Site 4
DIVAR AN series
MIX (up to 4 x DIVAR AN + 1 x DIP AIO)
Site 5
Site 7
DIP AIO 7000
Site 8
DIP AIO 5000
Site 6
DEVICES
5 max
per site
CONNECTION ON DEMAND
(max 20 simultaneous connections / client)
Use VPN or SSH (Device port forwarding not recommended due to security risks!)
NO
ALARM
NO
STATUS
Setup DVR cameras profil and bandwidth limits accordings to the available bandwidth and simultaneous video streams to be transmitted via WAN
BVMS Server + DIP AIO 7000
Site 9
Up to 16 local recording cameras
BVMS Blueprints
Notes: The BVMS management server hosts an address book of unmanaged sites. The operator client loads the address book but does not connect to a site until it is instructed to do so by the system operator. Unmanaged sites can be another BVMS system, DIVAR IP all-in-one, DVR, or a group of cameras. For this use-case we have tested the BVMS management server on Microsoft Azure.

## Slide 18
MOBILE APP
BVMS
Unmanaged sites
Notes: Unmanaged sites offers, compared to BVMS Enterprise, reduced functionality but increased scalability.

## Slide 19: Video Security App
Operator client
BVMS Server
CAMERAS
2000
max
CLIENTS
100
max
VRM
125
max
VRM Server
Building A “VRM A”
DIVAR IP AIO (w/ VRM)
iSCSI array NETAPP
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
BVMS Blueprints
Building B “VRM B”
VIDEO SECURITY app (iOS & Android)
Connections made from Video Security app to each VRM – proper network configuration (ie. VPN) required.
Within VIDEO SECURITY app single site should not contain more, than 256 cameras.
In case of bigger BVMS Professional systems, cameras should be logically distributted to folders, each containing up to 256 cameras.

## Slide 20
BVMS APPLIANCES
DIVAR IP all-in-one 4000
DIVAR IP all-in-one 6000 / 7000
Notes: DIVAR IP all-in-one is BVMS in a box.

## Slide 21: DIVAR IP AIO 4000
Operator client
CAMERAS
32
max
CLIENTS
5
max
BVMS
VRM
VSG
iSCSI
HW DYNAMIC TRANSCODING
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
Up to 2 DIVAR IP AIO 4000 storage expansions per system.
Expansion
2
max
BVMS Blueprints
VIDEO SECURITY APP (iOS & Android)
DIVAR IP AIO 4000
DIVAR IP AIO 4000
DIVAR IP AIO 4000
Notes: The DIVAR IP AiO 4000 can handle up to 32 cameras and can have two additional storage extensions to ensure the required retention time can be stored. The hardware transcoding service allows the Video Security Client to connect to the DIVAR IP AiO 4000.

## Slide 22: DIVAR IP AIO 6000 + Storage
DIVAR IP AIO 6000
Operator client
CAMERAS
64
max
CLIENTS
20
max
BVMS
VRM
VSG
iSCSI
HW DYNAMIC TRANSCODING
Expansion
2
max
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
VRM
VSG
iSCSI
HW DYNAMIC TRANSCODING
BVMS Blueprints
VIDEO SECURITY APP (iOS & Android)
DIVAR IP AIO
Notes: The DIVAR IP AiO 6000 can handle up to 64 cameras and can have additional storage extensions to ensure the required retention time can be stored. The hardware transcoding service allows the Video Security Client to connect to the DIVAR IP AiO 6000.

## Slide 23: DIVAR IP AIO 7000 + Storage
Operator client
CAMERAS
256
max
CLIENTS
10
max
BVMS
VRM
VSG
iSCSI
HW DYNAMIC TRANSCODING
Expansion
4
max
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
VRM
VSG
iSCSI
HW DYNAMIC TRANSCODING
BVMS Blueprints
VIDEO SECURITY APP (iOS & Android)
DIVAR IP AIO 7000
DIVAR IP AIO 7000
Notes: The DIVAR IP AiO 7000 can handle up to 256 cameras and can have additional storage extensions to ensure the required retention time can be stored. The hardware transcoding service allows the Video Security Client to connect to the DIVAR IP AiO 7000.

## Slide 24
VIDEO STREAMING GATEWAY
BVMS OPENNESS
Notes: BVMS is an ONVIF Profile S compliant client. The Video Streaming Gateway acts as an ONVIF bridge between the ONVIF cameras and the rest of the components in BVMS.

## Slide 25: Video Streaming Gateway
Operator client
BVMS Server
CHANNELS
32/VSG
max
DIVAR IP AIO (VSG include)
Overall max 550 Mbit
ONVIF
JPEG via HTTP
H264 via RTSP
VSG 01
VSG n
VRM B
VRM A
iSCSI array NETAPP
VRM Server
ONVIF
JPEG via HTTP
H264 via RTSP
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
BVMS Blueprints
Notes: Each Video Streaming Gateway can handle up to 32 video channels. One operating system can run up to 7 instances of the Video Streaming Gateway. One operating system can therefore handle up to 224 cameras. The Video Streaming Gateway can be virtualized as well, but this might impact its performance. The Video Streaming Gateway can connect to ONVIF cameras, retrieve video using JPEG via HTTP, or RTSP.

## Slide 26
ACCESS CONTROL INTEGRATION
BVMS & AMS
Notes: Did you know you can build an integrated access control and video management environment using software and hardware from Bosch?

## Slide 27: Unified security operation
BVMS Client
AMS Server & Database
BLACK = 100Mb
BLUE = 1Gb
ORANGE = Wiegand
GREEN = I/O
Switch
BVMS client
…
BVMS Server
VMS Storage
…
BVMS and AMS Client
Reception: Enrolment process and basic video verification
Security control room: Unified security operation Video & Access
Server room: BVMS and AMS servers coexist in separated servers
Distributed security devices
BVMS & AMS systems integrated
Notes: The access management system and BVMS can be combined in one system. We recommend using the BVMS operator client for operational security management while using the access management system client for cardholder management at the reception desk or facilities management.

## Slide 28
BVMS VIEWER
Notes: BVMS Viewer is a video viewing client for installations that do not require advanced security management functionality.

## Slide 29: BVMS Viewer
Bosch VMS Viewer
CAMERAS
500
max
CLIENTS
1
max
DIVAR AN series
DIVAR network and hybrid
BLACK = 100Mbit/s
BLUE = 1Gbit/s
GREEN = 1Gbit/s - 10Gbit/s
Free of charge:
16 live only / local storage cameras
5 Recording solutions (DVR, VRM device)
16 unmanaged sites (max 1 simultaneous connection)
Max limit: 500 cameras in logical tree.
SSite
Site
DIP AIO 5000
CONNECTION ON DEMAND
(max 1 simultaneous connection)
Live only / local storage
cameras
BVMS Blueprints
DIVAR IP AIO
Notes: BVMS Viewer can handle up to 500 cameras and connects directly to its subsystems. Compared to other BVMS versions BVMS Viewer does not have event and alarm management capabilities and does not have a server component that stores events.

## Slide 30: BVMS